## Slide 1: COMPUTER ORGANISATION (TỔ CHỨC MÁY TÍNH)
Boolean Algebra

## Slide 2: Acknowledgement
The contents of these slides have origin from School of Computing, National University of Singapore.
We greatly appreciate support from Mr. Aaron Tan Tuck Choy for kindly sharing these materials.

## Slide 3: Policies for students
These contents are only used for students PERSONALLY.
Students are NOT allowed to modify or deliver these contents to anywhere or anyone for any purpose.

## Slide 4: Recording of modifications
Minor change in slide 13 (replace new picture)
Currently, there are no modification on these contents.

## Slide 5: WHERE ARE WE NOW?
Number systems and codes
Boolean algebra
Logic gates and circuits
Simplification
Combinational circuits
Sequential circuits
Performance
Assembly language
The processor: Datapath and control
Pipelining
Memory hierarchy: Cache
Input/output
Preparation: 2 weeks
Logic Design: 3 weeks
Computer organisation

## Slide 6: CHECK LIST
Have you done the Quick Review Questions for Chapter 2 Number Systems and Code?
Have you attempted the Self-Assessment Exercise #1 on IVLE Assessment?
Have you clarified your doubts on IVLE forum?
Ready to do a pop quiz?

## Slide 7: BOOLEAN ALGEBRA
Boolean Algebra
Precedence of Operators
Truth Table
Duality
Basic Theorems
Complement of Functions
Standard Forms
Minterms and Maxterms
Canonical Forms
Read up DLD for details!

## Slide 8: DIGITAL CIRCUITS (1/2)
Two voltage levels
  High, true, 1, asserted
  Low, false, 0, deasserted
Signals in digital circuit
High
Low
Signals in analog circuit
A digital watch

## Slide 9: DIGITAL CIRCUITS (2/2)
Advantages of digital circuits over analog circuits
  More reliable (simpler circuits, less noise-prone)
  Specified accuracy (determinable)
  Abstraction can be applied using simple mathematical model – Boolean Algebra
  Ease design, analysis and simplification of digital circuit – Digital Logic Design

## Slide 10: TYPES OF LOGIC BLOCKS
Combinational: no memory, output depends solely on the input
  Gates
  Decoders, multiplexers
  Adders, multipliers
Sequential: with memory, output depends on both input and current state
  Counters, registers
  Memories

## Slide 11: BOOLEAN ALGEBRA
Boolean values:
  True (1)
  False (0)
Connectives
  Conjunction (AND)
    A  B; A  B
  Disjunction (OR)
    A + B; A  B
  Negation (NOT)
    ; A; A'
Truth tables
A | B | A  B
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
A | B | A + B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
A | A'
0 | 1
1 | 0
Logic gates
A
B
AB
A
B
A+B
A
A'

## Slide 12: AND (∙)
Do write the AND operator ∙ instead of omitting it.
  Example: Write a∙b instead of ab
  Why? Writing ab could mean it is a 2-bit value.

## Slide 13: LAWS OF BOOLEAN ALGEBRA
Identity laws
  A + 0 = 0 + A = A ; A  1 = 1  A = A
Inverse/complement laws
  A + A' = 1 ; A  A' = 0
Commutative laws
  A + B = B + A ; A  B = B  A
Associative laws
  A + (B + C) = (A + B) + C ; A  (B  C) = (A  B)  C
Distributive laws
  A  (B + C) = (A  B) + (A  C) ; A + (B  C) = (A + B)  (A + C)

## Slide 14: PRECEDENCE OF OPERATORS
Precedence from highest to lowest
  Not
  And
  Or
Examples:
  A  B + C = (A  B) + C
  X + Y' = X + (Y')
  P + Q'  R = P + ((Q')  R)
Use parenthesis to overwrite precedence. Examples:
  A  (B + C)
  (P + Q)'  R

## Slide 15: TRUTH TABLE
Provide a listing of every possible combination of inputs and its corresponding outputs.
  Inputs are usually listed in binary sequence.
Example
  Truth table with 3 inputs and 2 outputs
x | y | z | y + z | x  (y + z)
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 0
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 1 | 1

## Slide 16: PROOF USING TRUTH TABLE
Prove: x  (y + z) = (x  y) + (x  z)
  Construct truth table for LHS and RHS
  Check that column for LHS = column for RHS
x | y | z | y + z | x  (y + z) | x  y | x  z | (x  y) + (x  z)
0 | 0 | 0 |  |  |  |  | 
0 | 0 | 1 |  |  |  |  | 
0 | 1 | 0 |  |  |  |  | 
0 | 1 | 1 |  |  |  |  | 
1 | 0 | 0 |  |  |  |  | 
1 | 0 | 1 |  |  |  |  | 
1 | 1 | 0 |  |  |  |  | 
1 | 1 | 1 |  |  |  |  | 


## Slide 17: DUALITY
If the AND/OR operators and identity elements 0/1 in a Boolean equation are interchanged, it remains valid
Example:
  The dual equation of a+(bc)=(a+b)(a+c) is a(b+c)=(ab)+(ac)
Duality gives free theorems – “two for the price of one”. You prove one theorem and the other comes for free!
Examples:
  If (x+y+z)' = x'y'z' is valid, then its dual is also valid: (xyz)' = x'+y'+z'
  If x+1 = 1 is valid, then its dual is also valid: x0 = 0

## Slide 18: BASIC THEOREMS (1/2)
Idempotency
  X + X = X ; X  X = X
Zero and One elements
  X + 1 = 1 ; X  0 = 0
Involution
  ( X' )' = X
Absorption
  X + XY = X ; X(X + Y) = X
Absorption (variant)
  X + X'Y = X + Y ; X(X' + Y) = XY

## Slide 19: BASIC THEOREMS (2/2)
DeMorgan’s
  (X + Y)' = X'  Y' ; (X  Y)' = X' + Y'
DeMorgan’s Theorem can be generalised to more than two variables, example: (A + B + … + Z)' = A'  B'  …  Z'
Consensus
  XY + X'Z + YZ = XY + X'Z
  (X+Y)(X'+Z)(Y+Z) = (X+Y)(X'+Z)

## Slide 20: PROVING A THEOREM
Theorems can be proved using truth table, or by algebraic manipulation using other theorems/laws.
Example: Prove absorption theorem X + XY = X
  X + XY = X1 + XY (by identity) = X(1+Y) (by distributivity) = X(Y+1) (by commutativity) = X1 (by one element) = X (by identity)
By duality, we have also proved X(X+Y) = X

## Slide 21: BOOLEAN FUNCTIONS
Examples of Boolean functions (logic equations):
  F1(x,y,z) = xyz'
  F2(x,y,z) = x + y'z
  F3(x,y,z) = x'y'z + x'yz + xy'
  F4(x,y,z) = xy' + x'z
x | y | z | F1 | F2 | F3 | F4
0 | 0 | 0 | 0 |  |  | 
0 | 0 | 1 | 0 |  |  | 
0 | 1 | 0 | 0 |  |  | 
0 | 1 | 1 | 0 |  |  | 
1 | 0 | 0 | 0 |  |  | 
1 | 0 | 1 | 0 |  |  | 
1 | 1 | 0 | 1 |  |  | 
1 | 1 | 1 | 0 |  |  | 


## Slide 22: COMPLEMENT
Given a Boolean function F, the complement of F, denoted as F', is obtained by interchanging 1 with 0 in the function’s output values.
Example: F1 = xyz'
What is F1' ?

x | y | z | F1 | F1'
0 | 0 | 0 | 0 | 
0 | 0 | 1 | 0 | 
0 | 1 | 0 | 0 | 
0 | 1 | 1 | 0 | 
1 | 0 | 0 | 0 | 
1 | 0 | 1 | 0 | 
1 | 1 | 0 | 1 | 
1 | 1 | 1 | 0 | 

## Slide 23: STANDARD FORMS (1/2)
Certain types of Boolean expressions lead to circuits that are desirable from implementation viewpoint.
Two standard forms:
  Sum-of-Products
  Product-of-Sums
Literals
  A Boolean variable on its own or in its complemented form
  Examples: x, x', y, y'
Product term
  A single literal or a logical product (AND) of several literals
  Examples: x, xyz', A'B, AB, dg'vw

## Slide 24: STANDARD FORMS (2/2)
Sum term
  A single literal or a logical sum (OR) of several literals
  Examples: x, x+y+z', A'+B, A+B, c+d+h'+j
Sum-of-Products (SOP) expression
  A product term or a logical sum (OR) of several product terms
  Examples: x, x + yz', xy' + x'yz, AB + A'B', A + B'C + AC' + CD
Product-of-Sums (POS) expression
  A sum term or a logical product (AND) of several sum terms
  Examples: x, x(y+z'), (x+y')(x'+y+z), (A+B)(A'+B'), (A+B+C)D'(B'+D+E')
Every Boolean expression can be expressed in SOP or POS.

## Slide 25: DO IT YOURSELF
Put the right ticks in the following table.

Expression | SOP? | POS?
X'∙Y + X∙Y' + X∙Y∙Z |  | 
(X+Y')∙(X'+Y)∙(X'+Z') |  | 
X' + Y + Z |  | 
X∙(W' + Y∙Z) |  | 
X∙Y∙Z' |  | 
W∙X'∙Y + V∙(X∙Z + W') |  | 
SOP expr: A product term or a logical sum (OR) of several product terms.
POS expr: A sum term or a logical product (AND) of several sum terms.

## Slide 26: MINTERMS & MAXTERMS (1/2)
A minterm of n variables is a product term that contains n literals from all the variables.
  Example: On 2 variables x and y, the minterms are:
  x'∙y', x'∙y, x∙y' and x∙y
A maxterm of n variables is a sum term that contains n literals from all the variables.
  Example: On 2 variables x and y, the maxterms are:
  x'+y', x'+y, x+y' and x+y
In general, with n variables we have 2n minterms and 2n maxterms.

## Slide 27: MINTERMS & MAXTERMS (2/2)
The minterms and maxterms on 2 variables are denoted by m0 to m3 and M0 to M3 respectively.
Each minterm is the complement of the corresponding maxterm
  Example: m2 = x∙y' m2' = ( x∙y' )' = x' + ( y' )' = x' + y = M2
x | y | Minterms |  | Maxterms | 
 |  | Term | Notation | Term | Notation
0 | 0 | x'∙y' | m0 | x+y | M0
0 | 1 | x'∙y | m1 | x+y' | M1
1 | 0 | x∙y' | m2 | x'+y | M2
1 | 1 | x∙y | m3 | x'+y' | M3

## Slide 28: CANONICAL FORMS
Canonical/normal form: a unique form of representation.
  Sum-of-minterms = Canonical sum-of-products
  Product-of-maxterms = Canonical product-of-sums

## Slide 29: SUM-OF-MINTERMS
Given a truth table, example:
x | y | z | F1 | F2 | F3
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 1
0 | 1 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 1
1 | 0 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 1 | 1
1 | 1 | 0 | 1 | 1 | 0
1 | 1 | 1 | 0 | 1 | 0
Obtain sum-of-minterms expression by gathering the minterms of the function (where output is 1).

F3 =
F1 = x∙y∙z' = m6
F2 =

## Slide 30: PRODUCT-OF-MAXTERMS
Given a truth table, example:
x | y | z | F1 | F2 | F3
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 1
0 | 1 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 1
1 | 0 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 1 | 1
1 | 1 | 0 | 1 | 1 | 0
1 | 1 | 1 | 0 | 1 | 0
Obtain product-of-maxterms expression by gathering the maxterms of the function (where output is 0).

F3 =
F2 = (x+y+z) ∙ (x+y'+z) ∙ (x+y'+z') = M0 ∙ M2 ∙ M3 = PM(0,2,3)

## Slide 31: CONVERSION
We can convert between sum-of-minterms and product-of-maxterms easily
Example: F2 = Sm(1,4,5,6,7) = PM(0,2,3)
Why? See F2' in truth table.
x | y | z | F2 | F2'
0 | 0 | 0 | 0 | 1
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 0
F2' = m0 + m2 + m3 Therefore, F2 = (m0 + m2 + m3)' = m0' ∙ m2' ∙ m3' (by DeMorgan’s) = M0 ∙ M2 ∙ M3 (mx' =Mx)

## Slide 32: READING ASSIGNMENT
Conversion of Standard Forms
  Read up DLD section 3.4, pg 57 – 58.

## Slide 33: Q&A